Fragment Analysis (Beckman CEQ)

Materials Needed: (for full 96 well plate)

Size 400 Standard

SLS Solution

Minteral Oil (comes with 400 Standard)

Separation Buffer

MilliQ Water

Procedure

- Run desired PCR for fragment analysis (microsatellite PCR)

- Run a 2.5% Gel according to Gel Protocol for Microsatellites to determine dilution scheme.

- If samples are of strong intensity, dilute those PCR products with MilliQ Water as follows:

D4 Dye – 80uL per sample

D3 Dye – 60uL per sample

D2 Dye – 50uL per sample

- If sample are not of strong intensity, lesser dilution may be required.  Note – for some samples, no dilution may be needed.

- Once diluted, add 1.2uL of each sample to corresponding well in Beckman 96 well plate using multi-channel pipettor.

- Prepare a master mix for the number of samples to be run, according to the following:

1 well = 0.5uL 400 Standard + 30uL SLS Solution

102 wells = 51uL 400 Standard + 3060uL SLS Solution

or

100 wells = 27.5uL 400 Standard + 3084uL SLS Solution (if need to save 400 Standard)

- Vortex Master Mix thoroughly.

- Quantitatively place master mix in deep well tray.

- Add 30uL Master mix to each well using 8 channel pipettor.

  - Usually will not have enough MMix for all 8 pipets for last column.  Instead, load 4 tips with 30uL of remaining MMix.  Once added to plate, add 30uL one by one to remaining wells in plate.

- Once added to all wells, cover with foil seal, making sure all wells are sealed properly.

- Vortex to remove any air bubbles.

- Add 1 drop mineral oil to each well.

- Sample Plate is ready.

- To prepare separation buffer plate, add total of 300uL separation buffer to each well (150uL x 2) using 8 channel pipettor.